## Slide 1: SUPR E-Harv Model Simulations
Chuhong Duan
ECE Department, University of Virginia
07/31/2012

## Slide 2: Storage Node Output Voltage Profile
Blocks being tested: TEG, Boost Converter & Storage • Vary TEG harvested voltage over time (hardware) • Vary load current over time (power being drawn by the load)
• Plot different output voltage vs time profiles

## Slide 3
Input read from csv file: harvester_data.csv (SUPR -> CSV)
Simulation Parameters and Conditions:
(can be changed from user-input interface)
Processing frequency: 200kHZ (Tsample = 5 us)
Number of samples: 6050 (0.035s)
Boost converter switch 1 on time = switch 2 on time = idle time = 3*Tsample
Boost converter inductance: 47 uH
Storage capacitor : 47nF
Assuming TEG voltage is constant (0.005 V over time)
Node threshold voltage = clamp voltage = 1.35V
Start-up voltage = 600mV
Block in SUPR
Simulation Model

## Slide 4: Boost Converter Output Current
Zoomed in
Boost converter output current is only greater than 0
when switch 2 is on & switch 1 is off

## Slide 5
Load Current Draw from Storage Capacitor
In simulation, load current is pushed back:
load is turned on when Vcap > = Vthreshold
Load current constructed in excel
Load current in Simulink Simulation

## Slide 6: Adjusted Load Current and Corresponding Node Voltage
Mode 1 :
charging cap
Mode 2 :
Turn on load once Vc = 1.35V

## Slide 7: Boost Converter Conversion Efficiency Profile
Impulses: due to BC input current zero switching and fast processing rate (6050 samples)
Envelope indicates conversion efficiencies over time when Ibc is not 0
28.7% - 43.09% over time
Larger the output voltage is, higher the efficiency

## Slide 8: Energy (J) on Capacitor & Instantaneous Power(W) Supplied to Cap Over Time
Average Power to Cap:
60 .05 uW
Average Power from Cap:
-48.7 uW

## Slide 9: Compare Storage Types
Blocks being tested: Boost Converter &Cap, Boost Converter & Re-chargeable Battery • Vary load current I_load (with current spikes and constant draw characteristics) • Measure performance through its node output voltage profile: lifetime, delay (waiting time between operation modes)

## Slide 10
Input read from csv file: harvester_data.csv (SUPR -> CSV)
Simulation Parameters and Conditions:
(can be changed from user-input interface)
Processing frequency: 200kHZ (Tsample = 5 us)
Number of samples: 6050 (0.035s)
Boost converter switch 1 on time = switch 2 on time = idle time = 3*Tsample
Boost converter inductance: 47 uH
Assuming TEG voltage is constant (0.005 V over time)
Node threshold voltage = clamp voltage = 1.35V
Initial battery voltage = 1 V / 1.35 V
Polarization constant = 0.0014 Ohms
Exponential voltage = 0.111 V
Exponential capacity = 2.307 As
Maximum battery capacity = 0.72 As
Battery internal resistance = 0.002 Ohms
Initial state of charge = 25% / 100%
Block in SUPR
Simulation Model

## Slide 11: Battery Voltage Over Time (charging only) Initial Voltage = 1V
Zoomed in
Initial voltage is less than the threshold voltage (1.35V)
0.035 s of simulation charges the battery
very slowly – load is not turned on
during simulation
Longer simulation time required
Small ripple due to boost converter current switching

## Slide 12: Battery Voltage Over Time (charging and discharging) Initial Voltage = 1.35V, no Vclamp
Assume fully charged initially
Although battery takes a long time to charge, the output voltage is a lot more stable when the same amount of current is drawn as the one drawn from the capacitor storage model

## Slide 13: Battery Voltage Over Time (discharging) Initial Voltage = 1.35V, no Vclamp
0.1mA more current drawn each time step
Output voltage decays steadily

## Slide 14: DC-DC Converter Efficiency Profile
Blocks being tested: DC-DC Converter
Vary load current I_load
Vary desired output voltage
Plot efficiency vs parameters above

## Slide 15
Input read from csv file: DCDC.csv (SUPR -> CSV)
Block in SUPR
Simulation Model
Simulation Parameters and Conditions:
(can be changed from user-input interface)
Aatmesh’s Internal Report Module
Processing frequency: 200kHZ (Tsample = 5 us)
Rated current Io = 20uA
Maximum output voltage = 1.35V
Minimum output voltage = 1.1 V
Maximum efficiency: 80%

## Slide 16: DC-DC Conversion Efficiency vs Changing Load Current (with VDD constant)

## Slide 17: DC-DC Conversion Efficiency vs Changing Output Voltage (with I_load constant)

## Slide 18: DC-DC Conversion Efficiency vs Changing Load Current and VDD
The model is capable of finding the efficiency of the DC-DC Converter at any combinations of VDD and I_load
Following graph combines the first two cases and plots efficiencies over simulation time